## Slide 1: The Finite Element Method
Overview of Technique
Sample Element Library
Errors Associated with the technique

## Slide 2: Finite Element Replaces the Actual Problem with a Simpler One.
Babylonians (1900-1680 B.C.E)
  Calculation of radius of circle, =3
  Closer approximation found, =3.125
Egyptian Papyrus
  (1800 B.C.E.) Correct formula for volume of a pyramid and area of a sphere
  (1500 B.C.E.) Egyptians using = 101/2 (3.16).
Archimedes of Syracuse (287-212 B.C.E)
  Pythagoream theorem and two regular polygons
    Inscribing and circumscribing, = to
    Chinese, (429-501)
  Zu Chongzhi/Tsu Chung Chik: 24,576-gon, =355/113
Notes: Archimedes uses of finite element to calculate volumes of solids brought him to the threshold of calculus.
Chinese independently developed the use of polygons to inscribe and circumscribe circles and averaging the results to compute Pi

## Slide 3: Finite Element Essential for Complex Structures.
Jet Powered Aircraft/Swept Winged Structures
  Force Methods (S. Levy, 1947)
    Based on elasticity theory: equilibrium of forces and continuity of displacements
  Direct Stiffness Formulations (H.U. Schuerch,1953)
  Stiffness Matrix Based on Assumed Displacements (Turner et al./Boeing, 1956)
FE Based on Principle of Minimum Potential Energy (1960’s)

## Slide 4: Small But Finite Well-Defined Substructures
Elements
Nodes
Notes: Continuous elastic structure
Continuum
Divided into small but finite well-defined substructures (elements)
Discretized
ELEMENTS  Material Properties, Geometry, Stress, Strain
NODES  Loads and Displacements

## Slide 5: Errors Associated with Elements
Computational
  round-off errors
  numerical integration error
Discretization
  geometric
  displacement distributions

## Slide 6: One Dimensional (Line) Elements
2 Nodes
2 Nodes
2 Nodes
Truss
Beam
Frame
Pin-ended bar in
tension or
compression
Bending
Axial, torsional,
bending. With or
without load
Stiffening.

## Slide 7: Two Dimensional (Surface) Elements
4 Nodes
4-node
quadrilateral
Plane stress or strain,
axisymmetry, shear
panel, thin flat plate
in bending
8 Nodes
8-node
quadrilateral
Plane stress or strain,
thin plate in bending
3 Nodes
3-node
triangular
Plane stress or strain,
axisymmetry, shear
panel, thin flat plate
in bending. Prefer quad where possible. Used for transitions of quads.
6 Nodes
6-node
triangular
Plane stress or strain,
axisymmetry, thin flat plate
or shell in bending. Prefer quad where possible.

## Slide 8: Three Dimensional (Solid) Elements
Hexagonal
(Brick)
Pentagonal
(Wedge)
Tetrahedron
(Tet)
8-nodes
6-nodes
4-nodes
Solid,
Thick plate
Solid,
Thick Plate,
Used for transitions
Solid,
Thick Plate,
Used for transitions
16-nodes
12-nodes
8-nodes

## Slide 9: Sample Special Purpose Elements
Gap
Hook
Rigid
2-Nodes
2-Nodes
Variable
Free displacement for
prescribed compressive gap
Free displacement for
prescribed extension gap
Rigid constraints
between nodes

## Slide 10: Energy Methods are Essential for Advanced Elements
Direct Stiffness Method
  Easy to understand physically
  More difficult to apply to complex element
Rayleigh-Ritz Method
  Based on energy methods
  Easier to implement on complex elements
  More flexibility in simulating load and boundary conditions