## Slide 1
6 m
3 m
8 m
30 kN
20 kN
15 kN
Use SolidWorks Simulation to determine
The force in each member of the truss.
The reactions at A and B.
Use any pipe Structural Member, Alloy Steel as the material, and answer the question: Does the cross-section change the force in the members?

## Slide 2
SOLUTION: Setting up the problem in SolidWorks Simulation and running the FEA Solver generates the following result.

## Slide 3
Under the Simulation Feature Manager, with the Right-Mouse-Button select “Results” and then select “List Beam Forces” to generate a table of loads on each element of the truss.

## Slide 4
Under the Simulation Feature Manager, with the Right-Mouse-Button select “Results” and then select “List Resultant Forces” to show the reactions where the constraints are applied.

## Slide 5
Under the Simulation Feature Manager “Results” tree, with the Right-Mouse-Button select “Probe” and then select members on the truss to show the stress in the member.
The stress in a member is a function of the cross-section; however, the force in each member is independent of cross-section.