## Slide 1
Chapter 7
Shafts and Shaft Components
Lecture Slides
© 2015 by McGraw-Hill Education. This is proprietary material solely for authorized instructor use. Not authorized for sale or distribution in any manner. This document may not be copied, scanned, duplicated, forwarded, distributed, or posted on a website, in whole or part.

## Slide 2: Chapter Outline

## Slide 3: Shaft Design
Material Selection
Geometric Layout
Stress and strength
  Static strength
  Fatigue strength
Deflection and rigidity
  Bending deflection
  Torsional deflection
  Slope at bearings and shaft-supported elements
  Shear deflection due to transverse loading of short shafts
Vibration due to natural frequency

## Slide 4: Shaft Materials
Deflection primarily controlled by geometry, not material
Stress controlled by geometry, not material
Strength controlled by material property

## Slide 5: Shaft Materials
Shafts are commonly made from low carbon, CD or HR steel, such as AISI 1020–1050 steels.
Fatigue properties don’t usually benefit much from high alloy content and heat treatment.
Surface hardening usually only used when the shaft is being used as a bearing surface.

## Slide 6: Shaft Materials
Cold drawn steel typical for d < 3 in.
HR steel common for larger sizes. Should be machined all over.
Low production quantities
  Lathe machining is typical
  Minimum material removal may be design goal
High production quantities
  Forming or casting is common
  Minimum material may be design goal

## Slide 7: Shaft Layout
Issues to consider for shaft layout
  Axial layout of components
  Supporting axial loads
  Providing for torque transmission
  Assembly and Disassembly
Fig. 7–1

## Slide 8: Axial Layout of Components
Fig. 7–2

## Slide 9: Supporting Axial Loads
Axial loads must be supported through a bearing to the frame.
Generally best for only one bearing to carry axial load to shoulder
Allows greater tolerances and prevents binding
Fig. 7–3
Fig. 7–4

## Slide 10: Providing for Torque Transmission
Common means of transferring torque to shaft
  Keys
  Splines
  Setscrews
  Pins
  Press or shrink fits
  Tapered fits
Keys are one of the most effective
  Slip fit of component onto shaft for easy assembly
  Positive angular orientation of component
  Can design key to be weakest link to fail in case of overload

## Slide 11: Assembly and Disassembly
Fig. 7–5
Fig. 7–6

## Slide 12: Assembly and Disassembly
Fig. 7–7
Fig. 7–8

## Slide 13: Shaft Design for Stress
Stresses are only evaluated at critical locations
Critical locations are usually
  On the outer surface
  Where the bending moment is large
  Where the torque is present
  Where stress concentrations exist

## Slide 14: Shaft Stresses
Standard stress equations can be customized for shafts for convenience
Axial loads are generally small and constant, so will be ignored in this section
Standard alternating and midrange stresses
Customized for round shafts

## Slide 15: Shaft Stresses
Combine stresses into von Mises stresses

## Slide 16: Shaft Stresses
Substitute von Mises stresses into failure criteria equation. For example, using modified Goodman line,
Solving for d is convenient for design purposes

## Slide 17: Shaft Stresses
Similar approach can be taken with any of the fatigue failure criteria
Equations are referred to by referencing both the Distortion Energy method of combining stresses and the fatigue failure locus name. For example, DE-Goodman, DE-Gerber, etc.
In analysis situation, can either use these customized equations for factor of safety, or can use standard approach from Ch. 6.
In design situation, customized equations for d are much more convenient.

## Slide 18: Shaft Stresses
DE-Gerber
where

## Slide 19: Shaft Stresses
DE-ASME Elliptic
DE-Soderberg

## Slide 20: Shaft Stresses for Rotating Shaft
For rotating shaft with steady bending and torsion
  Bending stress is completely reversed, since a stress element on the surface cycles from equal tension to compression during each rotation
  Torsional stress is steady
  Previous equations simplify with Mm and Ta equal to 0

## Slide 21: Checking for Yielding in Shafts
Always necessary to consider static failure, even in fatigue situation
Soderberg criteria inherently guards against yielding
ASME-Elliptic criteria takes yielding into account, but is not entirely conservative
Gerber and modified Goodman criteria require specific check for yielding

## Slide 22: Checking for Yielding in Shafts
Use von Mises maximum stress to check for yielding,
Alternate simple check is to obtain conservative estimate of s'max by summing s'a and s'm

## Slide 23: Example 7–1

## Slide 24: Example 7–1 (continued)

## Slide 25: Example 7–1 (continued)

## Slide 26: Example 7–1 (continued)

## Slide 27: Example 7–1 (continued)

## Slide 28: Estimating Stress Concentrations
Stress analysis for shafts is highly dependent on stress concentrations.
Stress concentrations depend on size specifications, which are not known the first time through a design process.
Standard shaft elements such as shoulders and keys have standard proportions, making it possible to estimate stress concentrations factors before determining actual sizes.

## Slide 29: Estimating Stress Concentrations

## Slide 30: Reducing Stress Concentration at Shoulder Fillet
Bearings often require relatively sharp fillet radius at shoulder
If such a shoulder is the location of the critical stress, some manufacturing techniques are available to reduce the stress concentration
  Large radius undercut into shoulder
  Large radius relief groove into back of shoulder
  Large radius relief groove into small diameter of shaft
Fig. 7–9

## Slide 31: Example 7–2

## Slide 32: Example 7–2 (continued)
Fig. 7–10

## Slide 33: Example 7–2 (continued)

## Slide 34: Example 7–2 (continued)

## Slide 35: Example 7–2 (continued)

## Slide 36: Example 7–2 (continued)

## Slide 37: Example 7–2 (continued)

## Slide 38: Example 7–2 (continued)

## Slide 39: Example 7–2 (continued)

## Slide 40: Example 7–2 (continued)

## Slide 41: Example 7–2 (continued)

## Slide 42: Example 7–2 (continued)

## Slide 43: Example 7–2 (continued)

## Slide 44: Example 7–2 (continued)

## Slide 45: Deflection Considerations
Deflection analysis at a single point of interest requires complete geometry information for the entire shaft.
For this reason, a common approach is to size critical locations for stress, then fill in reasonable size estimates for other locations, then perform deflection analysis.
Deflection of the shaft, both linear and angular, should be checked at gears and bearings.

## Slide 46: Deflection Considerations
Allowable deflections at components will depend on the component manufacturer’s specifications.
Typical ranges are given in Table 7–2

## Slide 47: Deflection Considerations
Deflection analysis is straightforward, but lengthy and tedious to carry out manually.
Each point of interest requires entirely new deflection analysis.
Consequently, shaft deflection analysis is almost always done with the assistance of software.
Options include specialized shaft software, general beam deflection software, and finite element analysis software.

## Slide 48: Example 7–3
Fig. 7–10

## Slide 49: Example 7–3 (continued)

## Slide 50: Example 7–3 (continued)
Fig. 7–11

## Slide 51: Example 7–3 (continued)

## Slide 52: Example 7–3 (continued)

## Slide 53: Adjusting Diameters for Allowable Deflections
If any deflection is larger than allowed, since I is proportional to d4, a new diameter can be found from
Similarly, for slopes,
Determine the largest dnew/dold ratio, then multiply all diameters by this ratio.
The tight constraint will be just right, and the others will be loose.

## Slide 54: Example 7–4

## Slide 55: Angular Deflection of Shafts
For stepped shaft with individual cylinder length li and torque Ti, the angular deflection can be estimated from
For constant torque throughout homogeneous material
Experimental evidence shows that these equations slightly underestimate the angular deflection.
Torsional stiffness of a stepped shaft is

## Slide 56: Critical Speeds for Shafts
A shaft with mass has a critical speed at which its deflections become unstable.
Components attached to the shaft have an even lower critical speed than the shaft.
Designers should ensure that the lowest critical speed is at least twice the operating speed.

## Slide 57: Critical Speeds for Shafts
For a simply supported shaft of uniform diameter, the first critical speed is
For an ensemble of attachments, Rayleigh’s method for lumped masses gives

## Slide 58: Critical Speeds for Shafts
Eq. (7–23) can be applied to the shaft itself by partitioning the shaft into segments.
Fig. 7–12

## Slide 59: Critical Speeds for Shafts
An influence coefficient is the transverse deflection at location I due to a unit load at location j.
From Table A–9–6 for a simply supported beam with a single unit load
Fig. 7–13

## Slide 60: Critical Speeds for Shafts
Taking for example a simply supported shaft with three loads, the deflections corresponding to the location of each load is
If the forces are due only to centrifugal force due to the shaft mass,
Rearranging,

## Slide 61: Critical Speeds for Shafts
Non-trivial solutions to this set of simultaneous equations will exist when its determinant equals zero.
Expanding the determinant,
Eq. (7–27) can be written in terms of its three roots as

## Slide 62: Critical Speeds for Shafts
Comparing Eqs. (7–27) and (7–28),
Define wii as the critical speed if mi is acting alone. From Eq. (7–29),
Thus, Eq. (7–29) can be rewritten as

## Slide 63: Critical Speeds for Shafts
Note that
The first critical speed can be approximated from Eq. (7–30) as
Extending this idea to an n-body shaft, we obtain Dunkerley’s equation,

## Slide 64: Critical Speeds for Shafts
Since Dunkerley’s equation has loads appearing in the equation, it follows that if each load could be placed at some convenient location transformed into an equivalent load, then the critical speed of an array of loads could be found by summing the equivalent loads, all placed at a single convenient location.
For the load at station 1, placed at the center of the span, the equivalent load is found from

## Slide 65: Example 7–5
Fig. 7–14

## Slide 66: Example 7–5 (continued)

## Slide 67: Example 7–5 (continued)

## Slide 68: Example 7–5 (continued)

## Slide 69: Example 7–5 (continued)
Fig. 7–14

## Slide 70: Example 7–5 (continued)

## Slide 71: Example 7–5 (continued)

## Slide 72: Setscrews
Setscrews resist axial and rotational motion
They apply a compressive force to create friction
The tip of the set screw may also provide a slight penetration
Various tips are available
Fig. 7–15

## Slide 73: Setscrews
Resistance to axial motion of collar or hub relative to shaft is called holding power
Typical values listed in Table 7–4 apply to axial and torsional resistance
Typical factors of safety are 1.5 to 2.0 for static, and 4 to 8 for dynamic loads
Length should be about half the shaft diameter

## Slide 74: Keys and Pins
Used to secure rotating elements and to transmit torque
Fig. 7–16

## Slide 75: Tapered Pins
Taper pins are sized by diameter at large end
Small end diameter is
Table 7–5 shows some standard sizes in inches
Table 7–5

## Slide 76: Keys
Keys come in standard square and rectangular sizes
Shaft diameter determines key size
Table 7–6

## Slide 77: Keys
Failure of keys is by either direct shear or bearing stress
Key length is designed to provide desired factor of safety
Factor of safety should not be excessive, so the inexpensive key is the weak link
Key length is limited to hub length
Key length should not exceed 1.5 times shaft diameter to avoid problems from twisting
Multiple keys may be used to carry greater torque, typically oriented 90º from one another
Stock key material is typically low carbon cold-rolled steel, with dimensions slightly under the nominal dimensions to easily fit end-milled keyway
A setscrew is sometimes used with a key for axial positioning, and to minimize rotational backlash

## Slide 78: Gib-head Key
Gib-head key is tapered so that when firmly driven it prevents axial motion
Head makes removal easy
Projection of head may be hazardous
Fig. 7–17

## Slide 79: Woodruff Key
Woodruff keys have deeper penetration
Useful for smaller shafts to prevent key from rolling
When used near a shoulder, the keyway stress concentration interferes less with shoulder than square keyway
Fig. 7–17

## Slide 80: Woodruff Key

## Slide 81: Woodruff Key

## Slide 82: Stress Concentration Factors for Keys
For keyseats cut by standard end-mill cutters, with a ratio of r/d = 0.02, Peterson’s charts give
  Kt = 2.14 for bending
  Kt = 2.62 for torsion without the key in place
  Kt = 3.0 for torsion with the key in place
Keeping the end of the keyseat at least a distance of d/10 from the shoulder fillet will prevent the two stress concentrations from combining.

## Slide 83: Example 7–6
Fig. 7–19

## Slide 84: Example 7–6 (continued)

## Slide 85: Example 7–6 (continued)

## Slide 86: Retaining Rings
Retaining rings are often used instead of a shoulder to provide axial positioning
Fig. 7–18

## Slide 87: Retaining Rings
Retaining ring must seat well in bottom of groove to support axial loads against the sides of the groove.
This requires sharp radius in bottom of groove.
Stress concentrations for flat-bottomed grooves are available in Table A–15–16 and A–15–17.
Typical stress concentration factors are high, around 5 for bending and axial, and 3 for torsion

## Slide 88: Limits and Fits
Shaft diameters need to be sized to “fit” the shaft components (e.g. gears, bearings, etc.)
Need ease of assembly
Need minimum slop
May need to transmit torque through press fit
Shaft design requires only nominal shaft diameters
Precise dimensions, including tolerances, are necessary to finalize design

## Slide 89: Tolerances
Close tolerances generally increase cost
  Require additional processing steps
  Require additional inspection
  Require machines with lower production rates
Fig. 1–2

## Slide 90: Standards for Limits and Fits
Two standards for limits and fits in use in United States
  U.S. Customary (1967)
    Metric (1978)
Metric version will be presented, with a set of inch conversions

## Slide 91: Nomenclature for Cylindrical Fit
Upper case letters refer to hole
Lower case letters refer to shaft
Basic size is the nominal diameter and is same for both parts, D=d
Tolerance is the difference between maximum and minimum size
Deviation is the difference between a size and the basic size
Fig. 7–20

## Slide 92: Tolerance Grade Number
Tolerance is the difference between maximum and minimum size
International tolerance grade numbers designate groups of tolerances such that the tolerances for a particular IT number have the same relative level of accuracy but vary depending on the basic size
IT grades range from IT0 to IT16, but only IT6 to IT11 are generally needed
Specifications for IT grades are listed in Table A–11 for metric series and A–13 for inch series

## Slide 93: Tolerance Grades – Metric Series
Table A–11

## Slide 94: Tolerance Grades – Inch Series
Table A–13

## Slide 95: Deviations
Deviation is the algebraic difference between a size and the basic size
Upper deviation is the algebraic difference between the maximum limit and the basic size
Lower deviation is the algebraic difference between the minimum limit and the basic size
Fundamental deviation is either the upper or lower deviation that is closer to the basic size
Letter codes are used to designate a similar level of clearance or interference for different basic sizes

## Slide 96: Fundamental Deviation Letter Codes
Shafts with clearance fits
  Letter codes c, d, f, g, and h
  Upper deviation = fundamental deviation
  Lower deviation = upper deviation – tolerance grade
Shafts with transition or interference fits
  Letter codes k, n, p, s, and u
  Lower deviation = fundamental deviation
  Upper deviation = lower deviation + tolerance grade
Hole
  The standard is a hole based standard, so letter code H is always used for the hole
  Lower deviation = 0 (Therefore Dmin = 0)
  Upper deviation = tolerance grade
Fundamental deviations for letter codes are shown in Table A–12 for metric series and A–14 for inch series

## Slide 97: Fundamental Deviations – Metric series
Table A–12

## Slide 98: Fundamental Deviations – Inch series
Table A–14

## Slide 99: Specification of Fit
A particular fit is specified by giving the basic size followed by letter code and IT grades for hole and shaft.
For example, a sliding fit of a nominally 32 mm diameter shaft and hub would be specified as 32H7/g6
This indicates
  32 mm basic size
  hole with IT grade of 7 (look up tolerance DD in Table A–11)
  shaft with fundamental deviation specified by letter code g (look up fundamental deviation dF in Table A–12)
  shaft with IT grade of 6 (look up tolerance Dd in Table A–11)
Appropriate letter codes and IT grades for common fits are given in Table 7–9

## Slide 100: Description of Preferred Fits (Clearance)
Table 7–9

## Slide 101: Description of Preferred Fits (Transition & Interference)
Table 7–9

## Slide 102: Procedure to Size for Specified Fit
Select description of desired fit from Table 7–9.
Obtain letter codes and IT grades from symbol for desired fit from Table 7–9
Use Table A–11 (metric) or A–13 (inch) with IT grade numbers to obtain DD for hole and Dd for shaft
Use Table A–12 (metric) or A–14 (inch) with shaft letter code to obtain dF for shaft
For hole
For shafts with clearance fits c, d, f, g, and h
For shafts with interference fits k, n, p, s, and u

## Slide 103: Example 7–7

## Slide 104: Example 7–8

## Slide 105: Stress in Interference Fits
Interference fit generates pressure at interface
Need to ensure stresses are acceptable
Treat shaft as cylinder with uniform external pressure
Treat hub as hollow cylinder with uniform internal pressure
These situations were developed in Ch. 3 and will be adapted here

## Slide 106: Stress in Interference Fits
The pressure at the interface, from Eq. (3–56) converted into terms of diameters,
If both members are of the same material,
d is diametral interference
Taking into account the tolerances,

## Slide 107: Stress in Interference Fits
From Eqs. (3–58) and (3–59), with radii converted to diameters, the tangential stresses at the interface are
The radial stresses at the interface are simply
The tangential and radial stresses are orthogonal and can be combined using a failure theory

## Slide 108: Torque Transmission from Interference Fit
Estimate the torque that can be transmitted through interference fit by friction analysis at interface
Use the minimum interference to determine the minimum pressure to find the maximum torque that the joint should be expected to transmit.